## Slide 2: Contents
Contents
Introduction
Approach
  Intensity processing
  Depth processing
  Combination of proposals
Technologies
Development

## Slide 3: Left luggage detection
Detection of abandoned items in public places:
  Airports
  Train station
Issues:
  Shadows
  Occlusions
  Illumination changes
  Clutter
Introduction

## Slide 4: Pipeline
It is based on Reliable Left Luggage Detection Using Stereo Depth and Intensity Cues – C. Beleznai, P. Gemeiner and C. Zinner[1] of Austrian Institute of Technology
Approach
Intensity processing
Depth processing
Left luggage proposals
Video stream

## Slide 5: Intensity background modelling
The background model is computed by using the Zivkovic method [2]:
  Gaussian Mixture Model (GMM)
  Select dynamically the number of components
The left luggage are detected over time with the dual foregrounds model [3]:
  Two background models are computed
    : long-term background →
    : short-term background →
      e.g.: and
Intensity processing

## Slide 6: Dual foreground
Using and we have four cases for each pixel:
We aggregate the detection into an image
  It aims to remove noise in the detection;
  If , the pixel is marked as abandoned item.
Intensity processing
 |  | Background
 |  | Background pixel that was occluded
 |  | Static object
 |  | Foreground
 |  | Background
 |  | Background pixel that was occluded
 |  | Static object
 |  | Foreground

## Slide 7: Aggregator update rule
The aggregator update rule is the following:
A set of bounding box of intensity-based proposals is obtained.
Intensity processing
Update rule | Condition
 | Condition

## Slide 8: Depth processing
Background model is built over time using the accumulate running average method:
The spatial changes are accumulated in an aggregator.
The accumulator entry that have a number of observations above a threshold is marked as abandoned item.
A set of bounding box of depth-based proposals is obtained.
Approach
Original Frame

## Slide 9: Combination of proposals
The two sets of proposals generated by intensity and depth-based detection are merged by using:
where and are two overlapping bounding boxes in depth and intensity.
If an abandoned item is detected.
Approach

## Slide 10: Technologies
Video capture with Kinect device
  RGB camera:
    resolution
    bit quantization
  Depth sensor:
    resolution
    bit quantization
  USB 2.0 interface
OpenKinect
  Open source library
  Multiplatform
OpenCV
Technologies

## Slide 11: Intensity processing
We implement an intensity processing module.
The RGB processing routine can be summed as following:
    # get next video frame
    rgb.current_frame = cam.get_image()
    # get rgb dual foreground (long and short term)
    rgb.compute_foreground_masks(rgb.current_frame)
    # update rgb aggregator
    rgb.update_detection_aggregator()
    # extract bounding box proposals
    rgb_proposal_bbox = rgb.extract_proposal_bbox()
A bounding box contains a set of connected pixel which aggregator value is
The bounding boxes with area less than 50 pixel are filtered:
  So small objects are discarded.
Development

## Slide 12: Depth processing
The depth processing routine can be summed as following:
    # get next depth frame (11-bit precision)
    depth.current_frame = cam.get_depth_matrix()
    depth.current_frame_holes = bg_models.compute_holes_mask_in_frame(depth.current_frame)
    # get depth background
    depth.update_background_model(depth.current_frame, depth.current_frame_holes)
    # get depth foreground
    depth.extract_foreground_mask_from_run_avg(depth.current_frame)
    # apply opening to remove noise
    depth.foreground_mask = bg_models.apply_opening(depth.foreground_mask, BG_OPEN_KSIZE, cv2.MORPH_ELLIPSE) depth_proposal_bbox = depth.extract_proposal_bbox(depth.ACCUMULATOR)
    # cut foreground with real values
    foreground_depth_proposal = bg_models.cut_foreground(depth.current_frame, depth.foreground_mask)
Is it that simple? Would be nice!!!
Development

## Slide 13: Depth challenge
The depth video stream is noisy:
  We apply the opening morphological operator.
The depth video stream is not defined everywhere:
  it’s available for the image regions that are close enough to the device;
  for black objects the sensor can’t measure the depth value;
  A proper management of N/D pixel value is required:
    Per ogni frame … bla bla bla
Development

## Slide 14: Depth-based proposals
The spatial changes over time are accumulated in an image aggregator:
  If the aggregator exceeds a threshold is segmented[4] with a bounding box;
  The spatial region is marked as left item proposal.
We provide methods to accumulate the depth changes:
  Image Accumulator
  Bounding Box Accumulator
  Best Bounding Box Accumulator
Development

## Slide 15: Combination of proposals
The intensity and depth-based proposals sets are merged by using:
If an abandoned item is detected:
  The bounding box is saved in the set
Since in the RGB foreground model the left luggage become background in the long run the intensity-based proposals are discarded
  The last frame is saved
  The last set of bounding boxes of proposals is saved
  If
Development

## Slide 16: Test
Test

## Slide 17: Performance
Test

## Slide 18: References
[1] C. Beleznai, P. Gemeiner and C. Zinner, Reliable Left Luggage Detection Using Stereo Depth and Intensity Cues
[2] Z. Zivkovic and F. Heijden, Efficient adaptive density estimation per image pixel for the task of background subtraction
[3] F. Porikli, Y. Ivanov and T. Haga, Robust abandoned object detection using dual foregrounds
[4] Suzuki, S. and Abe, K., Topological Structural Analysis of Digitized Binary Images by Border Following. CVGIP 30 1, pp 32-46 (1985).
References

## Slide 19: Thanks
Left luggage detection
March xxth, 2014
Course of Multimedia Databases – a.a. 2013-14
Q & A
Andrea Rizzo, Matteo Bruni